## Slide 1
CanSat 2024 Preliminary Design Review (PDR)
TEAM PHOENIX
2024-ASI-CANSAT-012

## Slide 2
CANSAT configuration
147 MM
392MM
Camera
2nd circular PCB
3rd Circular PCB
1st Circular PCB
(Or)
Parachute Section
Payload
Gyro
Top Lib Opened
2nd Parachute deployed

## Slide 3
475m Detected
Altitude Check
Innovation adopted by your team
The CanSat still in contracted state from 1000 m to 475 m of altitude.
Unlocked position
locked position
The CanSat in the retracted state after the altitude of 475 m.
Automatic Expansion: CanSat expands at a specific altitude (475m).
Direct Atmosphere Exposure: Sensors exposed immediately for accurate readings.
Teensy Control: Teensy processor automates servo and lock mechanisms.
Compact Design: Expands only when needed, saving space.
Efficient Data Collection: Real-time atmospheric data at a critical altitude.
INNOVATION
Launch
Data Collection
Servo Trigger
Expansion

## Slide 4
The first parachute deploys when the Cant is released from the rocket
The first parachute deploys when the CanSat is released from the rocket
CANSAT descent control mechanism
The first parachute is folded on the CanSat's top lid and unfolds due to air resistance, reducing the descent velocity to 15 m/s
The first parachute deploys when the CanSat is released from the rocket
1st parachute deployment Mechanism
2nd parachute deployment Mechanism
locked position
Unlocked position
The parachute reduces the descent rate to 2 m/s.
At 500m altitude, the second parachute deploys using a servo lock mechanism.
The first parachute deploys when the sed from the rocket
At 475m altitude, the servo releases the lock, allowing the outer shell to retract downward.
Expansion Mechanism
1st Parachute Deploys
2nd Parachute Released
Expansion Mechanism Triggered
CanSat Reaches Ground
Deployed from Rocket
1000 m
500 m
475 m
0 m

## Slide 5
CUBE PARACHUTE
Velocity - 2 m/s
Velocity - 15m/s
- Primary Parachute
Hemispherical with spill hole - Secondary parachute
Parachute design and sizing
Descent velocity = 15 m/s
Weight = 0.85 kg
Area = 13.71 cm
Material Used = Nylon
Colour = Fluorescent Orange
Descent velocity = 2 m/s
Weight = 0.85 kg
Area = 2.522
Diameter = 1.263 m
Hole = 7%
Material Used = Nylon
Colour = Voilet
Stability: Offers better stability during descent due to its box-like shape, reducing oscillations.
Compact Design: Easy to fold and store, making it space-efficient for deployment.
Improved Stability: The spill hole design reduces instability and oscillations, allowing for a more controlled and stable descent.
Improved Control: The spill hole helps regulate descent speed and reduces jerking, offering more precise control over the landing process.
41.13 cm
13.71 cm
126.8 cm
8.8 cm

## Slide 6
AS7265x
BMX160
DC Motor
Power subsystem block diagram
Communication subsystem block diagram
CANSAT avionics systems

## Slide 7
CanSat Data
USB-
ADAPTOR
Digi XBEE pro - 900 MHz transmitter
Yagi antenna 900MHz (receiver)
Digi XBEE pro - 900 MHz receiever
CANSAT mission control software and ground systems.
Overview of Mission Control Software
Ground Systems
Programming Language:
C/C++ for payload hardware
Python for ground station
Development Environment:
Visual Studio Code
Python Script
Telemetry Transmission
Ground Station Dashboard
Control Logic
Data Processing
User Action (if needed)
Mission Control Software Flow map
FPV Camera transmitter
FPV Camera receiver
For live video telemetry:

## Slide 8
CANSAT Mass, Cost, Power Budget and Descent Time
Phase | Height | Descent Rate | Descent Time
1st Parachute released | 1000m - 500m | 15 m/s | 33.7 s
2nd Parachute released | 500m - 0m | 2 m/s | 250
 | Total Descent time |  | 283.7 seconds
Total mass of electrical subsystem (g) | 240.8 g
Total mass of mechanical subsystem(g) | 610 g
Total Mass | 850.8 g
Total cost of electrical subsystem | 28217
Total cost of mechanical subsystem | 7379
Total Mass | 35595
Total mAh = 1058
It consumes 1058 mAh of power to function for 1 Hour.
With 2800 mAh battery it can function for 2hrs 35 mins